## Slide 1: RTL8712(8188_8191_8192SU) USB Linux Driver Quick Installation Guide

## Slide 2: Software Package & Platform requirements
Software Package:
8712 linux driver (source code)
- support linux kernel version 2.6
8712 documents

## Slide 3
Software Package & Platform requirements
Platform requirements:
PC-Based Linux platform (i386)
8712 USB Linux driver supports Linux kernel version
: from 2.6.18 ~ 2.6.33

## Slide 4: HOW- TO: Setting up Linux environment
- Demonstration based on Linux Fedora 2.6.24
Part 1: make 8712 USB Linux driver
(1) step1: uncompress the “rtl8712_8188_8191_8192SU_usb_linux_v2.6.x.x.2010xxxx.tar.gz” file. (in “driver” directory)
> tar zxvf rtl8712_8188_8191_8192SU_usb_linux_v2.6.6.0.20100930.tar.gz

## Slide 5
(2) step2: make 8712 USB driver module
> make
(3) step3: clean the operation environment
> ./clean
(4) step4: insert 8712 USB modules
> insmod 8712u.ko

## Slide 6
(5) step5: enable wlan0 interface
  > ifconfig wlan0 up
(6) step6: setup IP address
> ifconfig wlan0 192.168.1.100

## Slide 7
Part 2: Site Survey & connect to AP without security
step1: Site Survey
> iwlist wlan0 scan
(2) step2: Connect to AP
> iwconfig wlan0 essid “xxx”

## Slide 8
Notes: connect to AP using "Network Manager" GUI utility
  (a) Network Manager is a utility attempts to make use of wireless networking easy.
  (b) please disable the “Network Manager” when using command-line method to connect to AP, because the “Network Manager” will conflict with the method of command line.